## Slide 1
Input / Output Interface
Computer Organization & Architecture
An interface is a point of interaction or communication between two systems, devices, components, or users.
Why interfaces are needed: to allow the processor and peripheral devices to communicate, synchronize, and exchange data correctly.
Processor
I/O Interface
Peripheral Device

## Slide 2
What is an Interface?
Interface: It is a point of interaction or communication between two systems, devices, components, or users.
In computer systems, an interface provides the communication path and supporting logic needed to connect the processor with other components or peripheral devices.
Examples:
User Interface → menus + icons
Graphical Interface → windows, icons, menus
Hardware Interface → USB
Network Interface → NIC (Network Interface Card)

## Slide 3
Input / Output Interface: System View
Processor
Data
Address
Control
Interface
Keyboard and Display Terminal
Interface
Printers
Interface
Magnetic Disc
Buses
The processor communicates with interfaces over data, address, and control buses.

## Slide 4
Why Do We Use an I/O Interface?
CPU is very fast, while peripheral devices are slow. To synchronize the CPU and peripheral devices, we use an interface.
Keyboard sends data; the interface collects it and sends it collectively.
Processor + main memory are electronic/electronic devices, while some peripheral devices are electromechanical devices. They can have different signals; the interface integrates these signals.
For making data words compatible to the processor.
To harmonize the instruction logic of I/O devices for the processor.

## Slide 5
Interrupts
An interrupt is a signal sent to the CPU by software or hardware to temporarily pause its current program/task so that an important event can be serviced.
Basic idea:
Interrupt Occurs
CPU temporarily pauses current task
Execute Interrupt Service Routine (ISR)
Return to program
ISR = Interrupt Service Routine: the routine that handles the interrupt.

## Slide 6
1. Hardware Interrupts
A hardware interrupt is generated by a hardware device to request the CPU's attention.
In the 8085, TRAP, RST 7.5, and RST 6.5 are hardware interrupt pins that generate interrupt signals.
TRAP has the highest priority among the 8085 hardware interrupts listed here.
Examples: pressing a keyboard key, mouse click, USB drive activity.
Keyboard sends an interrupt
CPU temporarily pauses its task
Executes the ISR
CPU returns to the interrupted program

## Slide 7
2. Software Interrupts
A software interrupt is generated by a program or instruction.
The INT instruction is commonly used to generate a software interrupt.
Example: INT 21H (commonly used in DOS-era x86 programming for operating-system services).
The software interrupt causes the CPU to transfer control to an interrupt service routine and then return to the program.
Program
Software interrupt instruction
CPU
Interrupt Service Routine
Return to program
Note from the notes: Software interrupt was described as having higher priority than hardware interrupts. In actual processor architectures, priority rules depend on the specific CPU/interrupt mechanism.

## Slide 8
3. Vectored Interrupts
A vectored interrupt is an interrupt in which the CPU can directly identify the address of the Interrupt Service Routine (ISR).
The interrupt vector provides the address or reference needed to locate the appropriate ISR.
Because the ISR location can be obtained directly, vectored interrupts are generally faster and more organized.
Interrupt Occurs
Interrupt Vector
ISR Address Located
ISR Executes

## Slide 9
4. Non-Vectored Interrupts
In a non-vectored interrupt, the ISR address is not directly supplied by the interrupt.
The CPU needs additional steps to determine the interrupt source and the appropriate ISR.
An interrupt controller or other mechanism may be used to identify which device requested service.
The CPU then determines the address of the appropriate ISR.
Non-vectored interrupts are generally slower than vectored interrupts because additional identification steps are required.
Interrupt
Identify source
Determine ISR address
Execute ISR
Return

## Slide 10
CPU Steps in a Non-Vectored Interrupt
1. Interrupt occurs — a device sends an interrupt request to the CPU.
2. CPU completes the current instruction.
3. CPU saves the current program state, such as the program counter and status information.
4. CPU acknowledges the interrupt.
5. CPU identifies the interrupt source.
6. CPU determines or obtains the address of the appropriate ISR.
7. CPU executes the ISR.
8. CPU restores the saved processor state.
9. CPU resumes the interrupted program.

## Slide 11
5. Maskable Interrupts
A maskable interrupt is a hardware interrupt that the CPU can temporarily ignore, disable, or postpone.
The CPU uses an interrupt mask or interrupt-enable mechanism to control whether the interrupt is accepted.
If enabled → CPU accepts and services the interrupt.
If disabled/masked → CPU temporarily ignores or delays the interrupt.
Example: a timer generates an interrupt, and the CPU can mask the interrupt temporarily while performing a critical operation.
Interrupt request
Check interrupt mask
Enabled → Service
Masked → Delay

## Slide 12
6. Non-Maskable Interrupts
A non-maskable interrupt (NMI) cannot normally be ignored or disabled by the CPU.
It is used for critical events where immediate attention is required.
The CPU must respond to the interrupt.
Example: a serious hardware failure or other critical hardware condition.
Critical hardware event
NMI signal
CPU responds

## Slide 13
Interrupt Types — Quick Comparison
Type | Generated / Identified By | Key Characteristic
Hardware | Hardware device | Device requests CPU attention
Software | Program / instruction | Requests a software/OS service
Vectored | Interrupt vector | CPU can locate ISR directly
Non-vectored | Interrupt + source identification | Additional steps needed to locate ISR
Maskable | Hardware interrupt | Can be temporarily disabled/delayed
Non-maskable | Critical hardware event | Cannot normally be ignored

## Slide 14
Key Takeaways
An I/O interface connects the processor with peripheral devices and helps synchronize communication.
Interfaces handle differences in speed, signals, data compatibility, and I/O-device logic.
An interrupt temporarily diverts CPU attention to an important event through an ISR.
Hardware interrupts originate from devices; software interrupts originate from programs/instructions.
Vectored interrupts provide a direct way to locate the ISR; non-vectored interrupts require additional identification steps.
Maskable interrupts can be temporarily disabled or delayed; non-maskable interrupts are reserved for critical events.