## Slide 1
Types of Flag Registers
Flag registers: These flags show status or result of an arithmetic or logical operation.
Flag register layout:
S | Z | – | AC | – | P | – | C | Y
Sign flag | Zero |  | Auxiliary carry |  | Parity |  | Carry | 
S → Sign flag Z → Zero AC → Auxiliary carry P → Parity C/Y → Carry

## Slide 2
1. Carry Flag
A = 10H → Hexadecimal
B = 20H
ADD B → AC + B → AC
AC = Accumulator
Binary example:
A = 10H = 0001 0000
B = 20H = 0010 0000
Result = 0011 0000
If D7 bit carries 0, Carry Flag will show 0; if it is 1, then it will be 1.

## Slide 3
Carry Flag — Binary Addition
 | D7 … D4 | D3 … D0
A = 10H | 0001 | 0000
B = 20H | 0010 | 0000
Result | 0011 | 0000
Upper nibble = D7–D4
Lower nibble = D3–D0
The Carry Flag depends on the carry out of the most significant bit (D7).

## Slide 4
2. Parity Bit
• If total number of 1's in result is even, then P = 1.
• If total number of 1's is odd, then P = 0.
Example:
Result = 0011 0000
Number of 1's = 2 (even)
Therefore, Parity = 1.

## Slide 5
3. Auxiliary Carry
A = 10H
B = 20H
Binary representation:
A = 0001 0000
B = 0010 0000
--------
0011 0000
Here we have to consider D3.
If D3 is 0, AC → 0.
If D3 is 1, AC → 1.

## Slide 6
4. Zero Flag
Example:
1000 0000
+ 1000 0000
------------
1 0000 0000
ADD 80H
When D7 is 0, then Zero Flag is 1; when it is 1, Zero Flag is 0.

## Slide 7
5. Sign Flag
Example:
1000 0000
+ 1000 0000
------------
0 0000 0000
The sign is determined by the most significant bit (D7).
If D7 bit is 0, then Sign Flag = 0 and the value is positive.
If D7 bit is 1, then Sign Flag = 1 and the value is negative.

## Slide 8
Summary of Flag Registers
Flag | Symbol | Purpose
Sign Flag | S | Indicates sign using D7
Zero Flag | Z | Indicates whether result is zero
Auxiliary Carry | AC | Carry involving the lower nibble / D3
Parity Flag | P | Shows whether number of 1s is even or odd
Carry Flag | C/Y | Indicates carry out of the most significant bit