## Slide 1
Floating-Point and Fixed-Point Representation
Explanatory presentation based on the two provided notes
FIXED-POINT
FLOATING-POINT
1

## Slide 2
1. Why Numerical Representation Matters
Computer systems must represent real numbers, including values with fractional parts.
Examples include 25.75, 3.14159 and 0.00125.
Two important approaches in the notes are fixed-point and floating-point representation.
The key difference is how the binary point is positioned and how much numerical range is available.
REAL NUMBER
Fixed Point
OR
Floating Point
2

## Slide 3
2. Fixed-Point Representation
In fixed-point representation, the position of the binary point is predetermined and remains fixed.
The number is treated as an integer part plus a fixed fractional part.
Example: 1010.1100₂ = 10.75₁₀.
Advantages: simple hardware, fast calculations, predictable precision.
Typical use in the notes: embedded and digital signal-processing systems.
1010
.
1100
Binary point stays in the same position
1010₂ = 10₁₀
.1100₂ = 0.75₁₀
Total = 10.75₁₀
3

## Slide 4
3. Floating-Point Representation
Floating-point representation allows the binary point to move according to an exponent.
It is analogous to scientific notation.
Decimal analogy: 6250 = 6.25 × 10³.
Binary example: 101.1₂ = 1.011₂ × 2².
General form in the notes: (−1)ˢ × M × 2ᴱ.
101.1₂
1.011₂
× 2²
Binary point effectively moves according to exponent
4

## Slide 5
4. IEEE 754 Single Precision
Sign 1 bit
Exponent 8 bits
Fraction 23 bits
Sign indicates whether the value is positive or negative.
Exponent controls the scale/position of the binary point.
Fraction stores the fractional/significant bits.
Total = 1 + 8 + 23 = 32 bits.
| Sign | Exponent | Fraction |
5

## Slide 6
5. Explicit vs. Implicit Representation
EXPLICIT REPRESENTATION
IMPLICIT REPRESENTATION
Relevant information is directly stored or shown.
Example: normalized significand 1.011 explicitly shows the leading 1.
Some information is understood from the format and need not be stored.
In normalized IEEE 754 binary numbers, the leading 1 is hidden/implicit.
Actual: 1.011 → Stored fraction: 011000…
6

## Slide 7
6. Why Is the Leading 1 Implicit?
A normalized binary number has the form 1.xxxxx × 2ᴱ.
Because the first digit is always 1, IEEE 754 does not store that digit.
This saves one bit.
Single precision therefore has an effective 24-bit significand: 1 implicit bit + 23 stored fraction bits.
1.xxxxx × 2ᴱ
1 = implicit / hidden
xxxxx = stored fraction
Effective significand = 1 + 23 = 24 bits
7

## Slide 8
7. Fixed-Point vs. Floating-Point
Feature | Fixed Point | Floating Point
Binary point | Fixed | Moves according to exponent
Representation | Integer + fixed fraction | Sign + exponent + fraction
Range | Relatively limited | Very large
Precision | Fixed scale | Depends on magnitude
Hardware | Simpler | More complex
Typical uses | Embedded / DSP | Scientific computing / graphics / AI
8

## Slide 9
8. Worked Example: 5.5 in IEEE 754
1
Decimal → Binary
5.5 = 101.1₂
2
Normalize
101.1₂ = 1.011₂ × 2²
3
Sign
Positive → Sign = 0
4
Biased exponent
2 + 127 = 129 = 10000001₂
5
Fraction
01100000000000000000000
Final: 0 | 10000001 | 01100000000000000000000
9

## Slide 10
9. Example 1 — Represent 5.5
Step 1: Integer part: 5₁₀ = 101₂.
Step 2: Fractional part: 0.5₁₀ = 0.1₂.
Therefore: 5.5₁₀ = 101.1₂.
Step 3: Normalize: 101.1₂ = 1.011₂ × 2².
Step 4: Sign = 0; exponent = 2 + 127 = 129 = 10000001₂.
Fraction = 01100000000000000000000.
5.5 → 101.1₂
1.011₂ × 2²
0 | 10000001 | 01100000000000000000000
10

## Slide 11
10. Example 2 — Represent 10.25
Step 1: Integer part: 10₁₀ = 1010₂.
Step 2: Fractional part: 0.25₁₀ = 0.01₂.
Therefore: 10.25₁₀ = 1010.01₂.
Step 3: Normalize: 1010.01₂ = 1.01001₂ × 2³.
Step 4: Sign = 0; biased exponent = 3 + 127 = 130 = 10000010₂.
Fraction = 01001000000000000000000.
10.25 → 1010.01₂
1.01001₂ × 2³
0 | 10000010 | 01001000000000000000000
11

## Slide 12
11. Example 3 — Represent 0.625
Convert the fraction by repeated multiplication by 2:
0.625 × 2 = 1.25 → 1
0.25 × 2 = 0.50 → 0
0.50 × 2 = 1.00 → 1
Therefore: 0.625₁₀ = 0.101₂.
Normalize: 0.101₂ = 1.01₂ × 2⁻¹.
Biased exponent: −1 + 127 = 126 = 01111110₂.
0.625 → 0.101₂
1.01₂ × 2⁻¹
Exponent = 126
0 | 01111110 | 01000000000000000000000
12

## Slide 13
12. Example 4 — Represent −13.5
Step 1: 13₁₀ = 1101₂ and 0.5₁₀ = 0.1₂.
Therefore: 13.5₁₀ = 1101.1₂.
Step 2: Normalize: 1101.1₂ = 1.1011₂ × 2³.
Step 3: The number is negative → Sign = 1.
Biased exponent: 3 + 127 = 130 = 10000010₂.
Fraction = 10110000000000000000000.
−13.5 → 1101.1₂
1.1011₂ × 2³
Sign = 1
1 | 10000010 | 10110000000000000000000
13

## Slide 14
13. A General Conversion Workflow
Decimal number
Binary conversion
Normalize
Determine sign
Calculate biased exponent
Store fraction
32-bit IEEE 754
For normalized values: significand = 1.fraction The leading 1 is implicit and the 23-bit fraction is stored.
14

## Slide 15
14. Key Points to Remember
Fixed-point: the binary point is at a predetermined position.
Floating-point: the binary point effectively moves according to the exponent.
Explicit: information is directly represented or stored.
Implicit: information is known from the representation and need not be stored.
IEEE 754 single precision uses 1 sign bit, 8 exponent bits and 23 fraction bits.
For normalized binary values, the leading 1 is implicit, giving 24 effective significand bits.
The four worked examples show the same conversion pattern for positive, fractional and negative values.
15